# How to Replace a Shower Door Sweep

The sweep on your shower door helps to keep the water inside the shower. If it fails, water and soapy residue may leak onto your bathroom floor. Water leaks are never good for a home, but if the floor is tiled, water lying on the surface also makes it dangerous. Imagine turning off the water, opening the door, and stepping out onto a hard slippery floor surface. This is why it is important to replace the gasket as soon as you realize it is not serving its purpose.

1 - Purchase the right size of shower door sweep. Measure the thickness of the glass. When you purchase the sweep, check it is compatible with the thickness of glass in your shower door. Check also it is long enough for the shower door. It does not matter if it is too long as it can easily be cut, but it must not be too short.

2 - Establish whether the sweep is held in its channel by adhesive, or by a combination of adhesive and screws. If screws are present, remove them with a screwdriver before carefully scraping as much adhesive off the glass as possible with a putty knife.

3 - Grasp one end of the gasket and carefully free it from the shower door.

4 - Cut the new gasket to the correct length by measuring it against the old one. Lay both on the floor. Place the end of the new gasket against the end of the old one. Make a mark with a felt tip pen on the new gasket, at the point where the old one ends. Cut off the excess length of new gasket with scissors, being careful to keep the edge straight.

5 - Wash the area of the shower door around the sweep with soapy water until it is clean. Rinse thoroughly and make sure it is completely dry.

6 – If the new sweep has adhesive, remove the strip that covers adhesive on the back of the new sweep. Carefully position it. If there is a track for the sweep on the shower door, make sure you properly insert the new sweep into it. Replace any screws you removed to take off the old sweep.

Tip

- If you own a dry vapor steam cleaner, you can use it to clean the bottom of the shower door before placing the new sweep in position. These machines do not use detergents, so there's no danger of residue affecting the tackiness of the adhesive.

Warning

- Give the sweep a bit of time to become secure in its new position, otherwise it may become loose, and allow water to leak from the shower cubicle. Follow the manufacturer's instructions.