Removing Shower Doors

Shower doors are sheets of tempered glass (shatters into small pieces when it breaks) enclosed in aluminum metal frames used to enclose a shower. Several types are available with the most common being the sliding shower door, usually found on bathtubs, and one pivoting on a frame affixed to the shower wall. Yet another type is a frameless shower door. Frameless shower doors attach to hinges mounting to the shower wall or a fixed panel of glass. Removal of a shower door is sometimes necessary for repairs to the shower or for easier access when cleaning the tracks.

Frameless Shower Doors

- Always have two people remove a frameless shower door. This type of door is extremely heavy and needs to be handled carefully to avoid damaging it.

- Remove the anchors securing the door hinges to the wall. Shower doors attached to a separate panel of glass use a hinge that grasps or pinches the shower door. Loosen the screws or bolts on each hinge that secure the shower door to the glass pane with a screwdriver or nut driver to free the door.

- Carefully set the shower door away from the work area.

Dual Sliding Glass Shower doors

- Grasp both sides of the door with your hands from inside the tub.

- Lift the door straight up towards the overhead track as far as you can.

- Swing the bottom of the door out and away from the bottom track.

- Push the top of the door either forward or backwards to disengage the door's wheels from the overhead track. Once the wheels are disengaged from the track, lower the door and remove it.

- Place the shower door away from the work area, and repeat the process for the remaining door.

Single Pivot Shower Doors

- Locate the screw securing the pivot cap to the shower doorjamb and remove it. The pivot cap holds the pivot post or pivot mechanism in place. Removing the pivot cap allows the pivot post or mechanism to slide up and down.

- While firmly grasping the door, slide the pivot post down. Once you slide the pivot post down, the top of the door will be free from the pivot wall jamb.

- Swing the top of the door out and away from the frame affixed to the wall.

- Lift the door far enough for the remaining pivot post to clear the frame.

- Carefully place the shower door away from the work area.

Warning

- Shower doors can be heavy; grasp doors firmly when removing to avoid damage to the door or other surfaces.

- Never attempt to cut tempered glass as it will shatter. When shower glass breaks, it shatters into small pieces.